## Slide 1
Michael Hiegemann
27/10/2014
New Process to Model Thermo-physical Fluid Properties
ETHZ/UZH Computational Science Industry Week

## Slide 2: Agenda
Problem area: Power plant performance simulation
Problem statement
Questions, Ideas and Proposals
Data, Literature and Tools

## Slide 3: Agenda
Problem area: Power plant performance simulation
Problem statement
Questions, Ideas and Proposals
Data, Literature and Tools

## Slide 4: Power Plant Performance Simulation – Basic Aspects
Thermodynamic modeling needs to take into account
System boundary
Components
Interfaces between components, i.e.
  flow quantities
  pressure
  temperature
  thermo-physical properties of the working fluid (e.g. specific heat capacity, specific enthalpy, etc.)
Fuel
Air
Flue gas
Electricity
Coolant in
Coolant out
Fluid properties are an essential part of performance modeling

## Slide 5: Power Plant Performance Simulation – Basic Aspects
Precise performance prediction requires precise fluid models
Simulations are required for
  Component and plant design
  Tendering including guarantee
  Order execution
  Plant operation
Technical and commercial requirements asked for increasing accuracy of the performance prediction
  Accuracy to the per mille level is required for reasons of competitiveness
Simulation tool components
  Mathematical solver
  Component models (calibrated from plant experience feedback)
  Fluid models (correlated from empirical data)
Example: adiabatic turbine

## Slide 6: Thermo-physical Fluid Properties – Working Media
Many fluids and fluid properties are required by simulation …
“Well understood” media
  Air
  Water/Steam
  Flue gas
  Fuel gas, fuel oil, coals
  Solids (fly ash, slag, gypsum, limestone)
  Lube oil
  Hydrogen
Properties required for simulation
  Volumetric properties:
  Caloric properties:
  Transport properties:
  Combined:
“Challenging” media
  Sea water
  Geothermal fluids
  ORC fluids
  Molten salts
  Heat transfer fluids
  CO2 rich solutions

## Slide 7: Thermo-physical Fluid Properties – Media and Phases
… and multiple phases and mixtures make it even more complex
Media
  Pure fluids
  Mixtures
Fluid state: Comprises the liquid, the gaseous, the supercritical and most two-phase states
Mixture: Consists out of more than one chemical
Multi-Phase
  Two phases
  Three or more phases
Single Phase
  Solid
  Liquid
  Gaseous
  Supercritical

## Slide 8: Thermo-physical Fluid Properties – Measurements
Volumetric data
  Single phase: – Density measurements (magnetic suspension balance) at given pressure and temperature
  Two-phase: – Saturation data (VLE) measurements (saturation pressure and two densities at given temperature)
Caloric data, usually for single-phase
  : Calorimeters
  : Calorimeters
  : Travelling time measurements
  Heat of evaporation
High precision measurement are somewhat like an art

## Slide 9: Thermo-physical Fluid Properties – Correlation
Fundamental equations and
are obtained consistently as derivatives
– the Gibbs free energy enables the description of the single phase properties, e.g. for solids
– the Helmholtz free energy enables the description of the single and the two phase properties using Maxwell relations
The physical framework of the problem is given
The mathematical approximation of is open
Fundamental equations are state of the art for real fluids

## Slide 10: Thermo-physical Fluid Properties – Helmholtz Free Energy

## Slide 11: Thermo-physical Fluid Properties – Helmholtz Free Energy
Domain of definition with a “hole”, steep gradients at low densities
[K]
[kg/m3]
[J/kg]
611.657 Pa <= <= 100 MPa, 273.16 K <= <= 1073.15 K

## Slide 12: Thermo-physical Fluid Properties – Helmholtz Free Energy
Helmholtz function: red, ideal part: green, residual part: blue
[J/kg]
[K]
[kg/m3]

## Slide 13: Thermo-physical Fluid Properties – Helmholtz Free Energy
Reduced Helmholtz function: red, ideal part: green, residual part: blue

## Slide 14: Thermo-physical Fluid Properties – Maxwell Criteria
Points F to K and G to K form the saturation lines

## Slide 15: Agenda
Problem area: Power plant performance simulation
Problem statement
Questions, Ideas and Proposals
Data, Literature and Tools

## Slide 16: Problem statement – Problem Features
Fitting the Helmholtz function is an unusual approximation task
cannot be measured directly, but derivatives can
The function has a kind of hole (the two-phase area), and the position of it needs to be determined
There are requirements on the monotonic and asymptotic behaviours of the function and its derivatives
Constraints may need to be obeyed (e.g. the position of the triple point or of the critical point)
Temperature [K] and density cannot go below zero
varies by several orders of magnitude
Practical application aspects require to find a balance between correlation accuracy and computation speed

## Slide 17: Problem statement – Current Process
Current process is based on heuristic approach
Define “bank of terms”, i.e. a set of heuristically selected functions
Execute parameter fittings for a large number of different combinations of functions from the above set
Select “best” combination
Determine errors

## Slide 18: Problem statement – Industrial Formulations using Sub-regions
Workaround for faster evaluation
273.16 K
0.01°C
623.15 K
350°C
863.15 K
590°C
1073.15 K
800°C
611Pa/0.0006 bar
100 MPa/1000 bar
2273.15 K
2000°C
50 MPa/500 bar
5
16.5 MPa/165 bar
3
1
2
4
g(p,T)
g(p,T)
f(v,T)
g(p,T)

## Slide 19: Problem statement – Artifacts of the Industrial Formulations
Chart: T [°C]
| 1.001E-2 | 50 | 100 | 150 | 200 | 250 | 275 | 300 | 310 | 320 | 330 | 340 | 349.99990000000003
IFC67 Region 1 | 4.0948 | 4.1268 | 4.1631 | 4.239 | 4.379 | 4.637 | 4.8537 | 5.1891 | 5.3809 | 5.6259 | 5.9483 | 6.3891 | 7.0269
IFC67 Region 4/3 | 6.9877 | 7.5625 | 7.6608 | 7.6399 | 7.6046 | 7.5835 | 7.5836 | 7.6061 | 7.651 | 7.7183 | 7.808 | 8.6289 | 10.3718 | 14.1073 | 25.6611 | 60.7355 | 29.4519 | 18.0042 | 16.8177 | 15.8083 | 14.9385 | 14.1804 | 13.513 | 12.9204 | 12.39 | 11.9121 | 11.624
IFC67 Region 2 | 10.9899 | 10.559 | 9.237 | 7.4529 | 6.32 | 5.5518 | 5.0066 | 4.1731 | 3.707 | 3.1986 | 2.9433 | 2.8101 | 2.7383 | 2.6973 | 2.6723
IAPWS-IF97 Region 1 | 4.109 | 4.126 | 4.1633 | 4.2383 | 4.3758 | 4.6371 | 4.856 | 5.1883 | 5.3745 | 5.6099 | 5.9188 | 6.3448 | 6.98
IAPWS_IF-97 Region 3 | 6.975 | 7.0598 | 7.1493 | 7.2438 | 7.3438 | 7.4498 | 7.5624 | 7.6823 | 7.8103 | 7.9473 | 8.0944 | 9.0335 | 10.5651 | 13.618 | 23.184 | 70.9632 | 28.4614 | 17.2445 | 16.1152 | 15.1589 | 14.3384 | 13.6265 | 13.0025 | 12.4509 | 11.9595 | 11.5188 | 11.2517
IAPWS-IF97 Region 2 | 11.2192 | 10.7119 | 9.2401 | 7.4062 | 6.3206 | 5.6026 | 5.086 | 4.2552 | 3.7661 | 3.2354 | 2.9679 | 2.8168 | 2.7267 | 2.6725 | 2.6415
IFC67 and IAPWS-IF97 suffer from artifacts at the sub-region boundaries
Chart: 
| 350.00009999999997 | 351 | 352 | 353 | 354 | 355 | 356 | 357 | 358 | 359 | 360
IFC67 Region 4 | 6.9877 | 7.5625 | 7.6608 | 7.6399 | 7.6046 | 7.5835 | 7.5836 | 7.6061 | 7.651 | 7.7183 | 7.808
IFC67 Region 1 | 5.1891 | 5.3809 | 5.6259 | 5.9483 | 6.3891 | 7.0269
IAPWS-IF97 Region 3 | 6.975 | 7.0598 | 7.1493 | 7.2438 | 7.3438 | 7.4498 | 7.5624 | 7.6823 | 7.8103 | 7.9473 | 8.0944
IAPWS-IF97 Region 1 | 5.1883 | 5.3745 | 5.6099 | 5.9188 | 6.3448 | 6.98
Chart: 
| 350.00009999999997 | 351 | 352 | 353 | 354 | 355 | 356 | 357 | 358 | 359 | 360 | 365 | 370 | 375 | 380 | 385 | 390 | 395 | 396 | 397 | 398 | 399 | 400 | 401 | 402 | 403 | 403.65418951126333
IFC67 Region 3 | 6.9877 | 7.5625 | 7.6608 | 7.6399 | 7.6046 | 7.5835 | 7.5836 | 7.6061 | 7.651 | 7.7183 | 7.808 | 8.6289 | 10.3718 | 14.1073 | 25.6611 | 60.7355 | 29.4519 | 18.0042 | 16.8177 | 15.8083 | 14.9385 | 14.1804 | 13.513 | 12.9204 | 12.39 | 11.9121 | 11.624
IFC67 Region 2 | 10.9899 | 10.559 | 9.237 | 7.4529 | 6.32 | 5.5518 | 5.0066 | 4.1731 | 3.707 | 3.1986 | 2.9433 | 2.8101 | 2.7383 | 2.6973 | 2.6723
IAPWS-IF97 Region 3 | 6.975 | 7.0598 | 7.1493 | 7.2438 | 7.3438 | 7.4498 | 7.5624 | 7.6823 | 7.8103 | 7.9473 | 8.0944 | 9.0335 | 10.5651 | 13.618 | 23.184 | 70.9632 | 28.4614 | 17.2445 | 16.1152 | 15.1589 | 14.3384 | 13.6265 | 13.0025 | 12.4509 | 11.9595 | 11.5188 | 11.2517
IAPWS-IF97 Region 2 | 11.2192 | 10.7119 | 9.2401 | 7.4062 | 6.3206 | 5.6026 | 5.086 | 4.2552 | 3.7661 | 3.2354 | 2.9679 | 2.8168 | 2.7267 | 2.6725 | 2.6415
Region boundary | 15 | 0
250 bar

## Slide 20: Problem statement – Issues of Current Process
Missing link to the area of mathematical approximation theory
No exploitation of the properties of orthogonal function systems
  Wavy behaviour in some places
  Missing monotonic and asymptotic features in some areas
  Lots of further artefacts, i.e. spikes in the two-phase area
Higher number of functions does not necessarily increase the quality of the approximation
SLOW evaluation
Complex structure of the function and its derivatives
Process is not generic, i.e. there is a different functional form for the reference equation of each fluid

## Slide 21: Problem Statement – Behaviour in the Two-phase Region
Spikes in the two-phase area jeopardize flash calculations
[kg/m3]
[Pa]
1073.15 K
873.15 K
773.15 K
647.1 K
623.15 K
523.15 K
IAPWS-95

## Slide 22: Agenda
Problem area: Power plant performance simulation
Problem statement
Questions, Ideas and Proposals
Data, Literature and Tools

## Slide 23: Questions
Multiple inter-linked problem areas
How to identify an ansatz for ?
  Use analytic terms / non-analytic terms?
How to identify
  the quality of a measurement series?
  outliers?
How to define weights of a data point / data series?
How to make an accuracy / error statement?
What is a reasonable approximation criterion?
Use sequential or simultaneous approximation process?
How many data points are required for a good fit?

## Slide 24: Ideas and Proposals
Introduce and exploit interdisciplinary methodology
Use orthogonal polynomials
  “Unless you’re sure another set of basis functions is better, use Chebyshev polynomials.
  Unless you’re really, really sure that another set of basis functions is better, use Chebyshev polynomials.” J.P. Boyd, Chebyshev and Fourier spectral methods, p. 10: “Moral Principle 1”
Use coordinate transformations – to be identified
Define a sole form for approximations of , generically applicable to all fluids
  one code for evaluation, but different sets of series coefficients and parameters for coordinate transformations
Identify and exploit asymptotic behaviour
Identify consistency checks / plots
Allow for constraints

## Slide 25: Agenda
Problem area: Power plant performance simulation
Problem statement
Questions, Ideas and Proposals
Data, Literature and Tools

## Slide 26: Data, Literature and Tools
Span, R.: Multiparameter Equations of State, Springer 2000.
www.iapws.org (24000 data, IAPWS-95 formulation)
Wagner, W., Pruss, A.: The IAPWS formulation 1995 for the thermodynamic properties of ordinary water substance for general and scientific use, J. Phys. Chem. Ref. Data 31, No. 2, 387-535 (2002).
http://www.peter-junglas.de/fh/water95/index.html (IAPWS-95 in Matlab)
http://www.peter-junglas.de/fh/publications/Poster-11_junglas.pdf (discussion on artefacts of IAPWS-95)
Abdulagatov, (new data on properties of supercooled water, no further details yet)
Bain, R.W.: Steam Tables 1964, Physical properties of water and steam, 0-800°C, 0-1000 bars, H.M.S.O., Edinburgh,1964, and Bain, R.W.: The preparation of steam tables with the aid of a digital computer, J. mech. Engng. Sci. 3, No. 4, 289-294 (1961) (first use of Chebyshev series in this field)
http://en.wikipedia.org/wiki/Book:Thermodynamics
Hayes, J.G. (ed.): Numerical approximation to functions and data, The Athlone Press 1970 (discussion of 1D and 2D data fittings and the treatment of constraints to be imposed on an approximation).
Trefethen, L.N.: Approximation theory and approximation practice, SIAM 2012
http://www.chebfun.org and the references therein
http://www-personal.umich.edu/~jpboyd/aaabook_9500may00.pdf (Chebyshev and Fourier spectral methods, for coordinate transformations see chapters 16 and 17)

## Slide 27: This Week
Now the ball is in your court …
… we will be available for any support!